## Slide 1: Assembly Language (Lab 8)

## Slide 2: Agenda
[Review] Integer Arithmetic
  Shift
  Rotate
Hands On

## Slide 3: Shift instructions

## Slide 4: Shift Instructions
Logical Shift
Arithmetic Shift
Fills the newly created bit position with zero.
The newly created bit position is filled with a copy of the original number’s sign bit.

## Slide 5: Logical Shift
SHR destination, count
SHL destination, count
Notes: SHL (shift left) instruction
Performs a logical left shift on the destination operand, filling the lowest bit with 0. The highest bit is moved to the Carry flag, and the bit that was in the Carry flag is discarded
SHR (shift right) instruction
performs a logical right shift on the destination operand, replacing the highest bit with a 0. The lowest bit is copied into the Carry flag, and the bit that was previously in the Carry flag is lost

## Slide 6: Arithmetic Shift
SAR destination, count
SAL destination, count

## Slide 7: Shift operands
SHL reg , imm8
SHL mem , imm8
SHL reg , CL
SHL mem ,CL

## Slide 8: Fast Multiplication and Division
Shifting an unsigned integer left by n bits multiplies the operand by 2n
Shifting an unsigned integer right by n bits divides the operand by 2n
mov dl, 5
shl dl, 1
0 0 0 0 0 1 0 1  5
0 0 0 0 1 0 1 0  10
mov dl, 64
shr dl, 3
0 1 0 0 0 0 0 0  64
0 0 0 0 1 0 0 0  8
Notes: SHR calculates the quotient only

## Slide 9: Rotate instructions

## Slide 10: Rotate instruction
ROR destination,count
ROL destination,count
Notes: Rotate instructions are the same as logical shift instructions except that the lost bit from one end in shifting is inserted in the other end in rotating. They are called circular shift or simply rotation.
ROL (Rotate Left) Instruction
Shifts each bit to the left. The highest bit is copied into the Carry flag and the lowest bit position.
Bit rotation does not lose bits. A bit rotated off one end of a number appears again at the other end

## Slide 11: Rotate instruction
RCR destination,count
RCL destination,count
Notes: RCl :it moves the most signifincant bit to the carry flag then rotates that bit to the least significant bit
Assume that the carry bit is an extra bit in the operand and rotate the whole bits including the carry bit.
CLC clears the carry flag
STC sets the carry flag

## Slide 12: Shift and rotate
Write a sequence of instructions that shift three memory bytes to the right by 1 bit position. Use the following data definition:
byteArray BYTE 81h,20h,33h
Notes: Based on section 7.3.1 (extended-precision integer) Shifting an extended-precision integer that has been divided into an array of bytes, words,or doublewords
Consider that you have a big number consists of 3 bytes and you can only access it using the variable’s name and you want to shift this number
byteArray BYTE 81h,20h,33h .code shr byteArray+2,1 rcr byteArray+1,1 rcr byteArray,1

## Slide 13: Shift and rotate
Write a sequence of instructions that shift three memory words to the left by 1 bit position.
Use the following data definition:
wordArray WORD 810Dh, 0C064h,93ABh
Notes: Based on section 7.3.1 (extended-precision integer)
wordArray WORD 810Dh,0C064h,93ABh .code shl wordArray,1 rcl wordArray+2,1 rcl wordArray+4,1

## Slide 14: Shift and rotate
Write ASM instructions that calculate
EAX * 24
using binary multiplication.
Notes: mov ebx,eax ; save a copy of eax shl eax,4 ; multiply by 16 shl ebx,3 ; multiply by 8 add eax,ebx ; add the products

## Slide 15: Shift and rotate
Write ASM instructions that calculate
EAX * 21
using binary multiplication.
Notes: Hint: 21 = 2^4+ 2^2 + 2^0.
mov ebx,eax ; save a copy of eax mov ecx,eax ; save another copy of eax shl eax,4 ; multiply by 16 shl ebx,2 ; multiply by 4 add eax,ebx ; add the products add eax,ecx ; add original value of eax

## Slide 16: Hands On

## Slide 17: 1. String to Binary Number
Write an assembly program the converts an 8–character string entered by user into a binary number.
Your should display an error message if the string contains a character that can not be converted to a binary digit.
Functions: ReadString, WriteBin
Enter a string: “10000001”
The Binary Value = 10000001
Enter a string: “10020001”
Invalid Input !!

## Slide 18: 2. Calculate the summation of Even or Odd integers
Write an assembly program that takes from the user 10 integers and calculates the summation of the even or odd numbers depends on his choice.
    Enter the array: 3 7 4 0 5 7 -5 6 1 10
    Even or Odd(E/O): E
    Summation of Even numbers = 20
    ---------------------------------------------
    Enter the array: 3 7 4 0 5 7 -5 6 1 10
    Even or Odd(E/O): O
    Summation of Even numbers = 18

## Slide 19: 3. Calculate the average
Write an assembly program that calculates the approximated integer average of 2^n integers read from the user where n = {1,2,3,…etc}.
You will first take from the user the size of the array he will enter and then the array.
The maximum number of integers to input is 64
    Enter the array size: 4 -> 2*2
    Enter the array: 4 6 8 3 -> (4+6+8+3) / 4 = 5.25
    The average = 5
    -----------------------------------------------------
    Enter the array size: 8
    Enter the array: 8 6 10 4 7 64 8 3
    The average = 13

## Slide 20: A BONUS task on the last Hands On
Write an assembly function that checks whether the input size is a power of 2 or not before executing the program.
If the number is a power of 2 then ecx = 0, otherwise ecx = 1.
    Enter the array size: 5
    Invalid input size !!
    -----------------------------------------------------
    Enter the array size: 8
    Enter the array: 8 6 10 4 7 64 8 3
    The average = 13

## Slide 21: Questions?

## Slide 22: Thanks!