## Slide 1: Assembly Language (Lab 4)

## Slide 2: Agenda
[Review] Addressing Modes
Status Flags
Branching (Unconditional)
Loop
Hands On
  Copy Reverse
  Draw Rectangle of Stars

## Slide 3: General Instruction Format
Let’s remember …

## Slide 4: General Instruction Format
Because the number of operands may vary, we can further subdivide the formats to have zero, one, two, or three operands. Here, we omit the label and comment fields for clarity:
  mnemonic
  mnemonic [destination]
  mnemonic [destination], [source]
  mnemonic [destination], [source-1], [source-2]
  [label:] mnemonic [operands][ ; comment ]

## Slide 5: General Instruction Format
To give added flexibility to the instruction set, x86 assembly language uses different types of instruction operands.
The following are the easiest to use:
  Immediate uses a numeric literal expression.
  Register uses a named register in the CPU.
  Memory references a memory location.

## Slide 6: Addressing Modes

## Slide 7
Addressing Modes Types
Register Addressing
Immediate Addressing
Direct Memory Addressing
In-Direct Memory Addressing
Direct Offset Addressing

## Slide 8
Operators
PTR
OFFSET
LENGTHOF
TYPE
SIZEOF
Notes: TYPE  array element has how many bytes for size, 1, 2,4 or 8
LENGTHOF  How many elements in an array
SIZEOF  returns array length in terms of bytes or LENGTHOF * Type
OFFSET  variable address
PTR  Override the default size of an operand, it reminds me with type casting

## Slide 9: Quirks
  .data
var DWORD 12345678h
  .code
  main PROC
    MOV ax, var
    ;?
    MOV ax, WORD PTR var
    ;loads 5678h
    MOV WORD PTR var, 4321h
    ; saves 4321h
    MOV ESI, OFFSET var
    MOV [ESI], 4321h
    ;?
Notes: Last code doesn’t work because 4321h must fit it self in aspecific size

## Slide 10
Status Flags
Zero
Sign
Carry
Auxiliary Carry
Overflow
Parity

## Slide 11: Flags Affected by Addition and Subtraction
When executing arithmetic instructions, we often want to know something about the result.
Is it negative, positive, or zero? Is it too large or too small to fit into the destination operand?
Answers to such questions can help us detect calculation errors that might otherwise cause erratic program behavior

## Slide 12: Flags Affected by Addition and Subtraction
We use the values of CPU status flags to check the outcome of arithmetic operations.
We also use status flag values to activate conditional branching instructions, the basic tools of program logic

## Slide 13: Flags Affected by Addition and Subtraction
Imagine This
High level language
If(x –y == 0)
{
Do something;
}
Else
{
Do another;
}
Assembly Like
If ZERO Flag == 1
GOTO LabelName1
//this will be the else part
LabelName1
So, Yes
Flags
Controls
branching
Notes: Zero flag =1 means that the result of the operation is =0

## Slide 14: Zero Flag
The Zero Flag (ZF) indicates that an operation produced zero.
For example, if an operand is subtracted from another of equal value, the Zero flag is set.

## Slide 15
  INCLUDE Irvine32.inc
  .code
  main PROC
  mov ecx, 1
  sub ecx, 1
  ; ECX = 0, ZF = 1
  mov eax, 0FFFFFFFFh
  inc eax
  ; EAX = 0, ZF = 1
  inc eax
  ; EAX = 1, ZF = 0
  dec eax
  ; EAX = 0, ZF = 1
  exit
  main ENDP
  END main
Zero Flag

## Slide 16: Carry Flag
The Carry Flag (CF) indicates unsigned integer overflow.
For example, if an instruction has an 8-bit destination operand but the instruction generates a result larger than 11111111 binary, the Carry flag is set.

## Slide 17: Carry Flag – Addition Case
When adding two unsigned integers, the Carry flag is a copy of the carry out of the MSB of the destination operand.
  11111111
  CF
  00000001
  00000000
  1
  We can say CF = 1 when the sum exceeds the storage size of its destination operand

## Slide 18
  INCLUDE Irvine32.inc
  .code
  main PROC
  mov al, 0FFh
  add al, 1
  ; AL = 00, CF = 1
  mov ax, 00FFh
  add ax, 1
  ; AX = 0100h, CF = 0
  mov ax, 0FFFFh
  add ax, 1
  ; AX = 0000, CF = 1
  exit
  main ENDP
  END main
Carry Flag – Addition Case
Notes: 0 before F means that a number not a letter

## Slide 19
  A subtract operation sets the Carry flag when a larger unsigned integer is subtracted from a smaller one.
  Carry Flag – Subtraction
  00000001 1
  CF
  00000010 2
  11111111 FFh
  1
  00000001 1
  11111110 -2
  The carry out of
  bit 7 is inverted and placed in the Carry flag, so CF = 1
Notes: Cf=1 because you borrowed from outside

## Slide 20
  Carry Flag – Subtraction
  INCLUDE Irvine32.inc
  .code
  main PROC
  mov al, 1
  sub al, 2
  ; AL = FFh, CF = 1
  exit
  main ENDP
  END main
Notes: Cf=1

## Slide 21: Carry Flag Quirks
The INC and DEC instructions do not affect the Carry flag.
Applying the NEG instruction to a nonzero operand always sets the Carry flag.

## Slide 22: Auxiliary Carry Flag
The Auxiliary Carry Flag (AC) is set when a 1 bit carries out of position 3 in the least significant byte of the destination operand.
  AC
  00010000 10h
  1
  00000001 1
  00001111 0Fh
  The sum (10h) contains a 1 in bit position 4 that was carried out of bit position 3

## Slide 23
  INCLUDE Irvine32.inc
  .code
  main PROC
  mov al, 0Fh
  add al, 1
  ; AC = 1
  exit
  main ENDP
  END main
Auxiliary Carry Flag

## Slide 24: Parity Flag
The Parity Flag (PF) is set when the least significant byte of the destination has an even number of 1 bits, immediately after an arithmetic or boolean instruction has executed.

## Slide 25
  INCLUDE Irvine32.inc
  .code
  main PROC
  mov al, 10001100b
  add al, 00000010b
  ; AL = 10001110, PF = 1
  sub al, 10000000b
  ; AL = 00001110, PF = 0
  exit
  main ENDP
  END main
  After the ADD, AL contains binary 10001110 (four 0 bits and four 1 bits), and PF = 1
  After the SUB, AL contains binary 00001110 (five 0 bits and three 1 bits), and PF = 0
Parity Flag

## Slide 26
  The Sign Flag (SF) indicates that an operation produced a negative result.
  It is set when the result of a signed arithmetic operation is negative.
  In other words, if the most significant bit (MSB) of the destination operand is set, the Sign flag is set.
Sign Flag

## Slide 27
  INCLUDE Irvine32.inc
  .code
  main PROC
  mov eax, 4
  sub eax, 5
  ; EAX = -1, SF = 1
  mov bl, 1
  ; BL = 01h
  sub bl, 2
  ; BL = FFh, SF = 1
  exit
  main ENDP
  END main
  the Sign flag is a copy of the destination operand’s high bit
Sign Flag

## Slide 28: Overflow Flag
  The Overflow Flag (OF) indicates signed integer overflow.
  It is set when the result of a signed arithmetic operation overflows or underflows the destination operand.

## Slide 29: Overflow Flag
    mov al, +127
    add al, 1 ; OF = 1
    mov al, -128
    sub al, 1 ; OF = 1
  For example, the largest possible integer signed byte value is +127; adding 1 to it causes overflow, as the destination operand value does not hold a valid arithmetic result, and the Overflow flag is set:
  Similarly, the smallest possible negative integer byte value is -128. Subtracting 1 from it causes underflow, and the Overflow flag is set:

## Slide 30: Overflow Flag – Overflow Detection
  How the Hardware Detects Overflow?!
    OF = (carry out of the MSB) XOR (carry into the MSB)

## Slide 31
  We show that adding the 8-bit binary integers 10000000 and 11111111 produces :
  01111111 and CF = 1 so the resulting MSB = 0. In other words, 1 XOR 0 produces OF = 1.
  CF
  01111111
  1
  10000000
  11111111
  OF = Carry Out the MSB XOR Carry In high bit of result
    = 1 XOR 0
    = 1
Overflow Flag – Overflow Detection
  0

## Slide 32
  The NEG instruction produces an invalid result if the destination operand cannot be stored correctly.
  For example, if we move -128 to AL and try to negate it, the correct value +128 will not fit into AL. The Overflow flag is set, indicating that AL contains an invalid value:
  On the other hand, if 127 is negated, the result is valid and the Overflow flag is clear:
Overflow Flag – Overflow Detection
    mov al, -128 ; AL = 10000000b
    neg al ; AL = 10000000b, OF = 1
    mov al, +127 ; AL = 01111111b
    neg al ; AL = 10000001b, OF = 0

## Slide 33: JMP and LOOP Instruction
Let’s change the sequence of the program and make use of flags…

## Slide 34: Conditional Instructions
By default, the CPU loads and executes programs sequentially.
But the current instruction might be conditional, meaning that it transfers control to a new location in the program based on the values of CPU status flags (Zero, Sign, Carry, etc.).
A transfer of control (jump), or branch, is a way of altering the order in which statements are executed
Assembly language programs use conditional instructions to implement high-level statements such as IF statements and loops

## Slide 35: JMP
The JMP instruction causes an unconditional transfer to a destination, identified by a code label that is translated by the assembler into an offset (address).
When the CPU executes an unconditional transfer, the offset of destination is moved into the instruction pointer (EIP), causing execution to continue at the new location.
  JMP destination

## Slide 36: JMP
Jumps may be short (between –128 and +127 bytes), near (between –32,768 and +32,767 bytes from the instruction following the jump), or far (in a different code segment).
When the 80386+ processors are in FLAT memory model, short jumps range is from –128 to +127 bytes and near jumps range is from –2 to +2 gigabytes.

## Slide 37: JMP Example
Comment on this program …
INCLUDE Irvine32.inc
.data
.code main PROC
  L1:
    call DumpRegs
    jmp L1;go to L1 line of code
exit main ENDP END main
Notes: Infinite loop printing registers values

## Slide 38: LOOP
The LOOP instruction, formally known as Loop According to ECX Counter, repeats a block of statements a specific number of times.
ECX is automatically used as a counter and is decremented each time the loop repeats.
So expected before using any LOOP inst. We have to set the ECX to a specific value
  LOOP destination

## Slide 39: LOOP
The execution of the LOOP instruction involves two steps:
It subtracts 1 from ECX
It compares ECX to zero
If ECX is not equal to zero, a jump is taken to the label identified by destination
If ECX equals zero, no jump takes place, and control passes to the instruction following the loop

## Slide 40: Tracing
  INCLUDE Irvine32.inc
  .code
  main PROC
  mov ax, 0
  mov ecx, 5
  L1:
  inc ax
  loop Ll
  exit
  main ENDP
  END main
AX = 0
ECX = 5
AX = 1
ECX = 4
AX = 2
ECX = 3
AX = 3
ECX = 2
AX = 4
ECX = 1
AX = 5
ECX = 0

## Slide 41: Tracing Quirks …
  INCLUDE Irvine32.inc
  .code
  main PROC
  mov ax, 0
  mov ecx, 0
  L1:
  inc ax
  loop Ll
  exit
  main ENDP
  END main
AX = 0
ECX = 0
AX = 1
ECX = FFFFFFFFh
AX = 2
ECX = FFFFFFFEh
The loop repeats
4,294,967,296 times
If CX is the loop counter (in real-address mode), it repeats 65,536 times
…

## Slide 42: Hands on – Multiply array elements by 2
Indirect addressing mode
arr1 DWORD 10, 20, 30, 40, 50
LENGTHOF
This hands on calculates the multiplication of an array by 2. It first gets the offset of the array and stores it in ESI register. Then, initialize ECX by the length of the array. Within the loop, it multiplies the current element of the array by 2 then slides ESI to point to the next element of the array and so on till the ECX becomes zero.

## Slide 43: Hands On – Copy Reverse
Write an assembly program which copy a src string into a dest string in a reversed order
Sample Data:
  src BYTE 'Hello',0
  dest WORD LENGTHOF src DUP(?)
Built in Fns  WriteString
Notes: include irvine32.inc
.data
src BYTE 'Hello',0
dest WORD LENGTHOF src DUP(?)
.code
main proc
mov esi,offset src + lengthof src-2
mov edi,offset dest
mov ecx,lengthof src-1
l1:
mov eax,0
mov ax,word ptr[esi]
mov [edi],ax
mov eax,[edi]
call writechar
add edi,4
dec esi
loop l1
exit
main endp
end main

## Slide 44: Hands On – Rectangle of Stars
Write an assembly program which draw this rectangle
Sample Run
4
****
***
**
*
BulitIn fns  WriteChar, ReadDec/ReadInt

## Slide 45: Questions?!

## Slide 46: Thanks!