## Slide 1: Assembly Language (Lab 6)

## Slide 2: Agenda
Quiz
CMP Instruction
Conditional Branching
Section Exercises
Hands on

## Slide 3: QUIZ TIME
30 Minutes.

## Slide 4
Status Flags
Zero
Sign
Carry
Auxiliary Carry
Overflow
Parity

## Slide 5: CMP
Lets do some checks …

## Slide 6: CMP Instruction
The CMP instruction compares the destination operand to the source operand.
It performs an implied subtraction of a source operand from a destination operand.
Neither operand is modified.
CMP is a valuable tool for creating conditional logic structures.
  CMP destination, Source
Notes: Cmp -> operand1 – operand2
And the result is discarded while the flags are updated.

## Slide 7: CMP Conditions
The following restrictions on CMP instruction should be considered:
All combinations of operands are allowed except CMP mem, mem. It is not accepted.
Can't compare two segment registers.
Can't compare operands with different sizes.
Notes: - You cant compare 2 immediates.

## Slide 8: CMP Instruction
When two unsigned operands are compared, the Zero and Carry flags indicate the following relations between operands.
CMP Results | ZF | CF
Destination < source | 0 | 1
Destination > source | 0 | 0
Destination = source | 1 | 0
Notes: Cmp 5,6 zf=0 cf=1
Cmp 6,5 zf=0 cf=0
Cmp 6,6 zf=1 cf=0

## Slide 9: CMP Instruction Examples
mov ax, 10
cmp ax, 50
ZF = 0, CF = 1
mov ax, 1000
mov cx, 1000
cmp cx, ax
mov si, 105
cmp si, 50
ZF = 1, CF = 0
ZF = 0, CF = 0

## Slide 10: CMP Instruction
When two signed operands are compared, the Sign, Zero and Overflow flags indicate the following relations between operands.
CMP Results | Flags
Destination < source | SF ≠ OF
Destination > source | SF = OF
Destination = source | ZF = 1

## Slide 11: Update flags after each CMP
Exercise (1)
  INCLUDE Irvine32.inc
  .data
  x sdword ?
  .code
  main PROC
  mov ax, -7
  cmp ax, -2
  mov eax, +5
  mov x, -3
  cmp eax, x
  exit
  main ENDP
  END main
  ZF=0 OF=0 SF=1
  ZF=0 OF=0 SF=0
Notes: Dest < source so OF is not equal sf
Dest > source therefor OF=SF

## Slide 12: Conditional JMP
Two Steps are involved in executing a conditional statement
Comparison
Jump
An operation such as CMP, AND or SUB modifies the CPU status flags
Conditional jump instruction tests the flags and causes a branch to a new
address

## Slide 13: Conditional Jump Instructions
A conditional jump instruction branches to a destination label when a status flag condition is true.
If the flag condition is false, the instruction immediately following the conditional jump is executed. (Skipped)
  Jxxx destination

## Slide 14: Conditional Jump Instructions
xxx expresses the relation tested.
The following table shows the conditional Jump instructions.
  Jxxx destination
Relation | For Unsigned Data | For Signed Data
Equal /Zero | JE/JZ | 
Not Equal/ Not Zero | JNE/ JNZ | 
Above/ Greater | JA/JNBE | JG/JNLE
Above or Equal/ Greater or Equal | JAE/JNB | JGE/JNL
Below/ Less | JB/JNAE | JL/JNGE
Below or Equal/ Less or Equal | JBE/JNA | JLE/JNG
Notes: JNBE  Not Below or Equal
JNLE  Not Less or Equal
Note: var word 0d123h  0 at the beginning means to be a number not a character hexa number must start with zero ends with h if it starts with a,b,c,d,e,f

## Slide 15: Translating Standard Control structures
High level language
If( i==j )
{
X=10;
}
Else
{
Y=10;
}
Assembly
Mov eax,i
Cmp eax, j
Jne Else
Mov x,10
Jmp endif
Else:
Mov y,10
Endif:
--------
Notes: how to translate high level language program control statements into their equivalent in assembly language using CMP and conditional jump instructions (assuming unsigned values).

## Slide 16: Section Exercises

## Slide 17: Section Exercises
Assume the usage of unsigned integers in all exercises:
Notes: 1.
cmp ebx, ecx
jna next ;if not above (<=)
mov X, 1
next:
2.
cmp edx, ecx
ja L1 ;if above (>)
mov X, 1
jmp next
L1: mov X, 2
next:

## Slide 18: Section Exercises
3.Implement the following pseudocode in assembly
if( val1 > ecx ) AND ( ecx > edx ) X = 1 else X = 2;
Notes: Cmp val,ecx
Jna else
Cmp ecx,edx
Jna else
Mov x,1
Jmp next
Else: x,2
Next:

## Slide 19: Section Exercises
Notes: 4.
cmp ebx, ecx
ja L1 ;if above (if >). since OR, then if this is satisfied then X=1 right away
cmp ebx, val1 ;will come here if 1st condition isn’t satisfied, so will check 2nd condition
ja L1
mov X, 2 ;if neither condition was satisfied
jmp next
L1: mov X, 1
next:
3. (not in slides): AND condition
cmp val1, ecx
jna L1
cmp ecx, edx
jna L1
mov X,1
jmp next
L1: mov X, 2
next:

## Slide 20: Hands On
Let the Fun Begins :D…

## Slide 21: Find the Minimum Value
Write an assembly program that finds the minimum value in an integer array. The array is first entered by the user then the minimum value is printed on the screen.
Note:
  You Must use Procedures
  Largest value of any signed variable is the variable that its bits are all 1’s except the sign bit (the most significant bit). Therefore, largest signed BYTE value is 7FH (+127); largest signed WORD value is 7FFFH (+32767) and so on. (Can you predict the smallest value how it should be?)
  Enter array size: 5
  Enter array elements: -10 5 6 -20 1
  Min value: -20
Notes: We don’t need to store integer values entered by the user in an array to find the minimum value. We store them for demonstration purposes.
(Updated: sample run added. Note that there are notes under the sample run text box.)

## Slide 22: Student’s Grades
Write an assembly program that inputs a student’s score and prints her/his grade. The student will be “Excellent” if her/his score is between 90-100, “Very Good” if the score is between 80-89, “Good” if the score is between 70-79, “Fair” if the score is between 60-69, and “Fail” if the score is lower than 60.
Notes:
Assume scores are integers.
The program should also print an error message if the entered score is less than 0 or greater than 100.
  Enter score: 85
  Very good
  Enter score: -100
  Error: invalid input score
Notes:   - (Updated: sample run added. Note that there are notes under the sample run text box.)

## Slide 23: Thanks.
Questions?